Module 13 — Capstone Project: Production Firewall for a Three-Tier Application
Firewalld: Zero to Expert on RHEL 10
Red Hat Enterprise Linux 10 | Instructor Edition

---
Overview
This capstone project integrates everything from the course into a single, end-to-end deployment. You will design, implement, verify, and harden a complete firewall configuration for a three-tier web application using the lab nodes as production-equivalent hosts.
Estimated time: 3–5 hours Difficulty: Expert
[Speaker Notes: This capstone project integrates everything from the course into a single, end-to-end deployment. You will design, implement, verify, and harden a complete firewall configuration for a three-tier web application using the lab nodes as production-equivalent hosts. **Estimated time**: 3–5 hours **Difficulty**: Expert ---]

---
The Scenario
Your company is deploying a three-tier web application on bare-metal (modeled by your Podman lab nodes):
◆ Internet / External Users
◆ [node1] — Gateway/Load Balancer
◆ [eth0] [eth1 + eth2]
◆ External DMZ Internal
◆ 172.20.1.0/24 172.20.2.0/24 172.20.3.0/24
◆ [node2] [node3]
◆ Web/App Server Database Server
[Speaker Notes: ◆ Application architecture ◆ Management subnet 172.20.3.30 (node3's IP — use node3 as the management host for testing) ◆ Security requirements → Internet → node1: only TCP 80 and 443; all else DROP (no ICMP from internet) → node1 → node2: only TCP 8080 and ICMP for health checks → node2 → node3: only TCP 5432 → Management host → all nodes: SSH (22) + ICMP → All outbound allowed from all nodes (for package updates etc.) → Logging: all denied packets must be logged → Rate limiting: max 50 new HTTP(S) connections/second per source IP; violators blocked 10 minutes → NAT: node1 masquerades for DMZ and Internal networks going to internet → Lockdown: enabled on all nodes; only root and NetworkManager whitelisted → nftables audit: all config changes logged to auditd Your company is deploying a three-tier web application on bare-metal (modeled by your Podman lab nodes): Internet / External Users │ [node1] — Gateway/Load Balancer │ │ [eth0] [eth1 + eth2] External DMZ Internal 172.20.1.0/24 172.20.2.0/24 172.20.3.0/24 │ │ [node2] [node3] Web/App Server Database Server ### Application architecture | Tier | Host | Services | Allowed clients | |------|------|----------|----------------| | Gateway | node1 | HTTPS (443), HTTP→HTTPS redirect (80), SSH admin (22) | Internet (443/80), Management subnet only (22) | | Web/App | node2 | HTTP (8080), SSH admin (22) | node1 internal IP only (8080), Management subnet (22) | | Database | node3 | PostgreSQL (5432), SSH admin (22) | node2 IP only (5432), Management subnet (22) | ### Management subnet `172.20.3.30` (node3's IP — use node3 as the management host for testing) ### Security requirements 1. Internet → node1: only TCP 80 and 443; all else DROP (no ICMP from internet) 2. node1 → node2: only TCP 8080 and ICMP for health checks 3. node2 → node3: only TCP 5432 4. Management host → all nodes: SSH (22) + ICMP 5. All outbound allowed from all nodes (for package updates etc.) 6. Logging: all denied packets must be logged 7. Rate limiting: max 50 new HTTP(S) connections/second per source IP; violators blocked 10 minutes 8. NAT: node1 masquerades for DMZ and Internal networks going to internet 9. Lockdown: enabled on all nodes; only root and NetworkManager whitelisted 10. nftables audit: all config changes logged to auditd ---]

---
The Scenario
Tier	Host	Services	Allowed clients
Gateway	node1	HTTPS (443), HTTP→HTTPS redirect (80), SSH admin (22)	Internet (443/80), Management subnet only (22)
Web/App	node2	HTTP (8080), SSH admin (22)	node1 internal IP only (8080), Management subnet (22)
Database	node3	PostgreSQL (5432), SSH admin (22)	node2 IP only (5432), Management subnet (22)
[Speaker Notes: Tier | Host | Services | Allowed clients ------------------------------------------------------------ Gateway | node1 | HTTPS (443), HTTP→HTTPS redirect (80), SSH admin (22) | Internet (443/80), Management subnet only (22) Web/App | node2 | HTTP (8080), SSH admin (22) | node1 internal IP only (8080), Management subnet (22) Database | node3 | PostgreSQL (5432), SSH admin (22) | node2 IP only (5432), Management subnet (22)]

---
Part 1 — Design (No Commands Yet)
Before writing a single firewall-cmd, document your design.
◆ 1.1 — Zone assignment
Fill in this table with your planned zone-to-interface mappings:
◆ 1.2 — Policy requirements mapping
[Speaker Notes: Before writing a single `firewall-cmd`, document your design. ### 1.1 — Zone assignment Fill in this table with your planned zone-to-interface mappings: | Node | Interface | Network | Planned Zone | Reasoning | |------|-----------|---------|-------------|-----------| | node1 | eth0 | 172.20.1.0/24 | `external` | Internet-facing; DROP target | | node1 | eth1 | 172.20.2.0/24 | `dmz` | Semi-trusted DMZ servers | | node1 | eth2 | 172.20.3.0/24 | `internal` | Trusted internal network | | node2 | eth0 | 172.20.2.0/24 | `dmz` | Receives traffic from gateway | | node3 | eth0 | 172.20.3.0/24 | `internal` | Isolated database tier | ### 1.2 — Policy requirements mapping | Requirement | firewalld mechanism | Module reference | |-------------|--------------------|-----------------:| | Internet → node1 (443/80 only) | `external` zone services | Module 04 | | Block all else at node1 external | Zone target=DROP + LogDenied | Modules 03, 10 | | node1 → node2 (8080 + ICMP) | `dmz` zone policy or rich rule | Modules 05, 06 | | node2 → node3 (5432 only) | `internal` zone service | Module 04 | | Management SSH/ICMP everywhere | Source-based zone + service | Module 03 | | NAT / masquerade | external zone masquerade | Module 07 | | Rate limiting | Custom nftables meter | Module 12 | | Lockdown | lockdown-on + whitelist | Module 11 | | Logging denied | LogDenied=all | Module 10 | | Audit | auditctl on /etc/firewalld | Module 11 | ---]

---
Part 1 — Design (No Commands Yet)
Node	Interface	Network	Planned Zone	Reasoning
node1	eth0	172.20.1.0/24	external	Internet-facing; DROP target
node1	eth1	172.20.2.0/24	dmz	Semi-trusted DMZ servers
node1	eth2	172.20.3.0/24	internal	Trusted internal network
node2	eth0	172.20.2.0/24	dmz	Receives traffic from gateway
node3	eth0	172.20.3.0/24	internal	Isolated database tier
[Speaker Notes: Node | Interface | Network | Planned Zone | Reasoning ------------------------------------------------------------ node1 | eth0 | 172.20.1.0/24 | external | Internet-facing; DROP target node1 | eth1 | 172.20.2.0/24 | dmz | Semi-trusted DMZ servers node1 | eth2 | 172.20.3.0/24 | internal | Trusted internal network node2 | eth0 | 172.20.2.0/24 | dmz | Receives traffic from gateway node3 | eth0 | 172.20.3.0/24 | internal | Isolated database tier]

---
Part 1 — Design (No Commands Yet)
Requirement	firewalld mechanism	Module reference
Internet → node1 (443/80 only)	external zone services	Module 04
Block all else at node1 external	Zone target=DROP + LogDenied	Modules 03, 10
node1 → node2 (8080 + ICMP)	dmz zone policy or rich rule	Modules 05, 06
node2 → node3 (5432 only)	internal zone service	Module 04
Management SSH/ICMP everywhere	Source-based zone + service	Module 03
NAT / masquerade	external zone masquerade	Module 07
Rate limiting	Custom nftables meter	Module 12
Lockdown	lockdown-on + whitelist	Module 11
Logging denied	LogDenied=all	Module 10
Audit	auditctl on /etc/firewalld	Module 11
[Speaker Notes: Requirement | firewalld mechanism | Module reference ------------------------------------------------------------ Internet → node1 (443/80 only) | external zone services | Module 04 Block all else at node1 external | Zone target=DROP + LogDenied | Modules 03, 10 node1 → node2 (8080 + ICMP) | dmz zone policy or rich rule | Modules 05, 06 node2 → node3 (5432 only) | internal zone service | Module 04 Management SSH/ICMP everywhere | Source-based zone + service | Module 03 NAT / masquerade | external zone masquerade | Module 07 Rate limiting | Custom nftables meter | Module 12 Lockdown | lockdown-on + whitelist | Module 11 Logging denied | LogDenied=all | Module 10 Audit | auditctl on /etc/firewalld | Module 11]

---
Part 2 — Node 1 (Gateway) Configuration
◆ Step 2.1 — Verify lab is running and nodes are reachable
◆ Step 2.2 — Assign interfaces to zones on node1
◆ Step 2.3 — Configure the external zone
◆ Step 2.4 — Configure the DMZ zone on node1 (toward node2)
◆ Step 2.5 — Configure the internal zone on node1 (toward node3)
◆ Step 2.6 — Port forwarding: HTTPS on node1 → HTTP on node2
◆ Step 2.7 — Set up inter-zone policy (node1 as router)
◆ Step 2.8 — Rate limiting with custom nftables (on node1)
[Speaker Notes: ◆ Step 2.9 — Lockdown on node1 ### Step 2.1 — Verify lab is running and nodes are reachable ```bash ~/firewalld-lab/start-lab.sh podman exec node1 firewall-cmd --state podman exec node2 firewall-cmd --state podman exec node3 firewall-cmd --state ``` ### Step 2.2 — Assign interfaces to zones on node1 ```bash podman exec -it node1 bash firewall-cmd --get-active-zones ip addr show firewall-cmd --zone=external --add-interface=eth0 --permanent firewall-cmd --zone=dmz --add-interface=eth1 --permanent firewall-cmd --zone=internal --add-interface=eth2 --permanent firewall-cmd --reload firewall-cmd --get-active-zones ``` ### Step 2.3 — Configure the external zone ```bash firewall-cmd --zone=external --set-target=DROP --permanent firewall-cmd --zone=external --add-service=http --permanent firewall-cmd --zone=external --add-service=https --permanent firewall-cmd --zone=external --add-icmp-block=echo-request --permanent firewall-cmd --zone=external --add-icmp-block=echo-reply --permanent firewall-cmd --zone=external --remove-service=ssh --permanent 2>/dev/null || true firewall-cmd --zone=external --add-masquerade --permanent firewall-cmd --set-log-denied=all firewall-cmd --reload firewall-cmd --zone=external --list-all ``` ### Step 2.4 — Configure the DMZ zone on node1 (toward node2) ```bash firewall-cmd --zone=dmz --add-service=http --permanent firewall-cmd --zone=dmz --add-protocol=icmp --permanent firewall-cmd --zone=dmz --remove-service=ssh --permanent 2>/dev/null || true firewall-cmd --reload firewall-cmd --zone=dmz --list-all ``` ### Step 2.5 — Configure the internal zone on node1 (toward node3) ```bash firewall-cmd --zone=internal --add-service=ssh --permanent firewall-cmd --zone=internal --add-protocol=icmp --permanent firewall-cmd --zone=internal --add-source=172.20.3.30 --permanent firewall-cmd --reload firewall-cmd --zone=internal --list-all ``` ### Step 2.6 — Port forwarding: HTTPS on node1 → HTTP on node2 ```bash firewall-cmd --zone=external --add-forward-port=\ port=443:proto=tcp:toport=8080:toaddr=172.20.2.20 --permanent firewall-cmd --zone=external --add-forward-port=\ port=80:proto=tcp:toport=8080:toaddr=172.20.2.20 --permanent firewall-cmd --reload ``` ### Step 2.7 — Set up inter-zone policy (node1 as router) ```bash firewall-cmd --new-policy=ext-to-dmz --permanent firewall-cmd --policy=ext-to-dmz --add-ingress-zone=external --permanent firewall-cmd --policy=ext-to-dmz --add-egress-zone=dmz --permanent firewall-cmd --policy=ext-to-dmz --set-target=ACCEPT --permanent firewall-cmd --new-policy=dmz-to-ext --permanent firewall-cmd --policy=dmz-to-ext --add-ingress-zone=dmz --permanent firewall-cmd --policy=dmz-to-ext --add-egress-zone=external --permanent firewall-cmd --policy=dmz-to-ext --set-target=ACCEPT --permanent firewall-cmd --new-policy=int-to-ext --permanent firewall-cmd --policy=int-to-ext --add-ingress-zone=internal --permanent firewall-cmd --policy=int-to-ext --add-egress-zone=external --permanent firewall-cmd --policy=int-to-ext --set-target=ACCEPT --permanent firewall-cmd --reload firewall-cmd --list-all-policies ``` ### Step 2.8 — Rate limiting with custom nftables (on node1) ```bash cat > /etc/nftables.d/ratelimit.nft << 'EOF' table inet http_guard { set burst_blocked { type ipv4_addr flags dynamic, timeout timeout 10m comment "IPs auto-blocked for exceeding rate limit" } chain input_http_guard { type filter hook input priority -2; # Established connections skip rate check ct state established,related accept # Drop already-blocked sources immediately ip saddr @burst_blocked drop # Rate limit new HTTP/HTTPS connections tcp dport { 80, 443 } ct state new \ meter http_rate { ip saddr limit rate over 50/second burst 100 packets } \ add @burst_blocked { ip saddr } \ drop } } EOF nft -f /etc/nftables.d/ratelimit.nft nft list table inet http_guard ``` ### Step 2.9 — Lockdown on node1 ```bash cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF' <?xml version="1.0" encoding="utf-8"?> <whitelist> <command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/> <selinux context="system_u:system_r:NetworkManager_t:s0"/> <user id="0"/> </whitelist> EOF sed -i 's/^#*Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf firewall-cmd --reload firewall-cmd --query-lockdown # → yes ``` ---]

---
Part 2 — Node 1 (Gateway) Configuration — BASH
~/firewalld-lab/start-lab.sh
podman exec node1 firewall-cmd --state
podman exec node2 firewall-cmd --state
podman exec node3 firewall-cmd --state
podman exec -it node1 bash
firewall-cmd --get-active-zones
ip addr show
firewall-cmd --zone=external --add-interface=eth0 --permanent
firewall-cmd --zone=dmz --add-interface=eth1 --permanent
firewall-cmd --zone=internal --add-interface=eth2 --permanent
firewall-cmd --reload
firewall-cmd --get-active-zones
[Speaker Notes: ~/firewalld-lab/start-lab.sh podman exec node1 firewall-cmd --state podman exec node2 firewall-cmd --state podman exec node3 firewall-cmd --state podman exec -it node1 bash firewall-cmd --get-active-zones ip addr show firewall-cmd --zone=external --add-interface=eth0 --permanent firewall-cmd --zone=dmz --add-interface=eth1 --permanent firewall-cmd --zone=internal --add-interface=eth2 --permanent firewall-cmd --reload firewall-cmd --get-active-zones]

---
Part 2 — Node 1 (Gateway) Configuration — BASH
firewall-cmd --zone=external --set-target=DROP --permanent
firewall-cmd --zone=external --add-service=http --permanent
firewall-cmd --zone=external --add-service=https --permanent
firewall-cmd --zone=external --add-icmp-block=echo-request --permanent
firewall-cmd --zone=external --add-icmp-block=echo-reply --permanent
firewall-cmd --zone=external --remove-service=ssh --permanent 2>/dev/null || true
firewall-cmd --zone=external --add-masquerade --permanent
firewall-cmd --set-log-denied=all
firewall-cmd --reload
firewall-cmd --zone=external --list-all
firewall-cmd --zone=dmz --add-service=http --permanent
firewall-cmd --zone=dmz --add-protocol=icmp --permanent
firewall-cmd --zone=dmz --remove-service=ssh --permanent 2>/dev/null || true
firewall-cmd --reload
firewall-cmd --zone=dmz --list-all
[Speaker Notes: firewall-cmd --zone=external --set-target=DROP --permanent firewall-cmd --zone=external --add-service=http --permanent firewall-cmd --zone=external --add-service=https --permanent firewall-cmd --zone=external --add-icmp-block=echo-request --permanent firewall-cmd --zone=external --add-icmp-block=echo-reply --permanent firewall-cmd --zone=external --remove-service=ssh --permanent 2>/dev/null || true firewall-cmd --zone=external --add-masquerade --permanent firewall-cmd --set-log-denied=all firewall-cmd --reload firewall-cmd --zone=external --list-all firewall-cmd --zone=dmz --add-service=http --permanent firewall-cmd --zone=dmz --add-protocol=icmp --permanent firewall-cmd --zone=dmz --remove-service=ssh --permanent 2>/dev/null || true firewall-cmd --reload firewall-cmd --zone=dmz --list-all]

---
Part 2 — Node 1 (Gateway) Configuration — BASH
firewall-cmd --zone=internal --add-service=ssh --permanent
firewall-cmd --zone=internal --add-protocol=icmp --permanent
firewall-cmd --zone=internal --add-source=172.20.3.30 --permanent
firewall-cmd --reload
firewall-cmd --zone=internal --list-all
firewall-cmd --zone=external --add-forward-port=\
port=443:proto=tcp:toport=8080:toaddr=172.20.2.20 --permanent
firewall-cmd --zone=external --add-forward-port=\
port=80:proto=tcp:toport=8080:toaddr=172.20.2.20 --permanent
firewall-cmd --reload
[Speaker Notes: firewall-cmd --zone=internal --add-service=ssh --permanent firewall-cmd --zone=internal --add-protocol=icmp --permanent firewall-cmd --zone=internal --add-source=172.20.3.30 --permanent firewall-cmd --reload firewall-cmd --zone=internal --list-all firewall-cmd --zone=external --add-forward-port=\ port=443:proto=tcp:toport=8080:toaddr=172.20.2.20 --permanent firewall-cmd --zone=external --add-forward-port=\ port=80:proto=tcp:toport=8080:toaddr=172.20.2.20 --permanent firewall-cmd --reload]

---
Part 2 — Node 1 (Gateway) Configuration — BASH
firewall-cmd --new-policy=ext-to-dmz --permanent
firewall-cmd --policy=ext-to-dmz --add-ingress-zone=external --permanent
firewall-cmd --policy=ext-to-dmz --add-egress-zone=dmz --permanent
firewall-cmd --policy=ext-to-dmz --set-target=ACCEPT --permanent
firewall-cmd --new-policy=dmz-to-ext --permanent
firewall-cmd --policy=dmz-to-ext --add-ingress-zone=dmz --permanent
firewall-cmd --policy=dmz-to-ext --add-egress-zone=external --permanent
firewall-cmd --policy=dmz-to-ext --set-target=ACCEPT --permanent
firewall-cmd --new-policy=int-to-ext --permanent
firewall-cmd --policy=int-to-ext --add-ingress-zone=internal --permanent
firewall-cmd --policy=int-to-ext --add-egress-zone=external --permanent
firewall-cmd --policy=int-to-ext --set-target=ACCEPT --permanent
firewall-cmd --reload
firewall-cmd --list-all-policies
[Speaker Notes: firewall-cmd --new-policy=ext-to-dmz --permanent firewall-cmd --policy=ext-to-dmz --add-ingress-zone=external --permanent firewall-cmd --policy=ext-to-dmz --add-egress-zone=dmz --permanent firewall-cmd --policy=ext-to-dmz --set-target=ACCEPT --permanent firewall-cmd --new-policy=dmz-to-ext --permanent firewall-cmd --policy=dmz-to-ext --add-ingress-zone=dmz --permanent firewall-cmd --policy=dmz-to-ext --add-egress-zone=external --permanent firewall-cmd --policy=dmz-to-ext --set-target=ACCEPT --permanent firewall-cmd --new-policy=int-to-ext --permanent firewall-cmd --policy=int-to-ext --add-ingress-zone=internal --permanent firewall-cmd --policy=int-to-ext --add-egress-zone=external --permanent firewall-cmd --policy=int-to-ext --set-target=ACCEPT --permanent firewall-cmd --reload firewall-cmd --list-all-policies]

---
Part 2 — Node 1 (Gateway) Configuration — BASH
cat > /etc/nftables.d/ratelimit.nft << 'EOF'
table inet http_guard {
set burst_blocked {
type ipv4_addr
flags dynamic, timeout
timeout 10m
comment "IPs auto-blocked for exceeding rate limit"
}
chain input_http_guard {
type filter hook input priority -2;
# Established connections skip rate check
ct state established,related accept
# Drop already-blocked sources immediately
ip saddr @burst_blocked drop
# Rate limit new HTTP/HTTPS connections
tcp dport { 80, 443 } ct state new \
meter http_rate { ip saddr limit rate over 50/second burst 100 packets } \
add @burst_blocked { ip saddr } \
drop
}
}
EOF
[Speaker Notes: cat > /etc/nftables.d/ratelimit.nft << 'EOF' table inet http_guard { set burst_blocked { type ipv4_addr flags dynamic, timeout timeout 10m comment "IPs auto-blocked for exceeding rate limit" } chain input_http_guard { type filter hook input priority -2; # Established connections skip rate check ct state established,related accept # Drop already-blocked sources immediately ip saddr @burst_blocked drop # Rate limit new HTTP/HTTPS connections tcp dport { 80, 443 } ct state new \ meter http_rate { ip saddr limit rate over 50/second burst 100 packets } \ add @burst_blocked { ip saddr } \ drop } } EOF nft -f /etc/nftables.d/ratelimit.nft nft list table inet http_guard]

---
Part 2 — Node 1 (Gateway) Configuration — BASH (cont. 2)
nft -f /etc/nftables.d/ratelimit.nft
nft list table inet http_guard
[Speaker Notes: cat > /etc/nftables.d/ratelimit.nft << 'EOF' table inet http_guard { set burst_blocked { type ipv4_addr flags dynamic, timeout timeout 10m comment "IPs auto-blocked for exceeding rate limit" } chain input_http_guard { type filter hook input priority -2; # Established connections skip rate check ct state established,related accept # Drop already-blocked sources immediately ip saddr @burst_blocked drop # Rate limit new HTTP/HTTPS connections tcp dport { 80, 443 } ct state new \ meter http_rate { ip saddr limit rate over 50/second burst 100 packets } \ add @burst_blocked { ip saddr } \ drop } } EOF nft -f /etc/nftables.d/ratelimit.nft nft list table inet http_guard]

---
Part 2 — Node 1 (Gateway) Configuration — BASH
cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF'
<?xml version="1.0" encoding="utf-8"?>
<whitelist>
<command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/>
<selinux context="system_u:system_r:NetworkManager_t:s0"/>
<user id="0"/>
</whitelist>
EOF
sed -i 's/^#*Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf
grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf
firewall-cmd --reload
firewall-cmd --query-lockdown # → yes
[Speaker Notes: cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF' <?xml version="1.0" encoding="utf-8"?> <whitelist> <command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/> <selinux context="system_u:system_r:NetworkManager_t:s0"/> <user id="0"/> </whitelist> EOF sed -i 's/^#*Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf firewall-cmd --reload firewall-cmd --query-lockdown # → yes]

---
Part 3 — Node 2 (Web/App Server) Configuration
◆ Step 3.1 — Zone assignment
◆ Step 3.2 — DMZ zone: allow only port 8080 from node1
◆ Step 3.3 — Lockdown on node2
[Speaker Notes: ```bash podman exec -it node2 bash ``` ### Step 3.1 — Zone assignment ```bash firewall-cmd --zone=dmz --add-interface=eth0 --permanent firewall-cmd --reload ``` ### Step 3.2 — DMZ zone: allow only port 8080 from node1 ```bash firewall-cmd --zone=dmz --remove-service=ssh --permanent 2>/dev/null || true firewall-cmd --zone=dmz --remove-service=http --permanent 2>/dev/null || true firewall-cmd --zone=dmz --add-rich-rule=' rule family="ipv4" source address="172.20.2.10" port port="8080" protocol="tcp" accept' --permanent firewall-cmd --zone=dmz --add-rich-rule=' rule family="ipv4" source address="172.20.2.10" protocol value="icmp" accept' --permanent firewall-cmd --zone=dmz --add-rich-rule=' rule family="ipv4" source address="172.20.3.30" service name="ssh" accept' --permanent firewall-cmd --zone=dmz --set-target=DROP --permanent firewall-cmd --set-log-denied=all firewall-cmd --reload firewall-cmd --zone=dmz --list-all ``` ### Step 3.3 — Lockdown on node2 ```bash cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF' <?xml version="1.0" encoding="utf-8"?> <whitelist> <command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/> <user id="0"/> </whitelist> EOF grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf sed -i 's/^Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf firewall-cmd --reload ``` ---]

---
Part 3 — Node 2 (Web/App Server) Configuration — BASH
podman exec -it node2 bash
firewall-cmd --zone=dmz --add-interface=eth0 --permanent
firewall-cmd --reload
[Speaker Notes: podman exec -it node2 bash firewall-cmd --zone=dmz --add-interface=eth0 --permanent firewall-cmd --reload]

---
Part 3 — Node 2 (Web/App Server) Configuration — BASH
firewall-cmd --zone=dmz --remove-service=ssh --permanent 2>/dev/null || true
firewall-cmd --zone=dmz --remove-service=http --permanent 2>/dev/null || true
firewall-cmd --zone=dmz --add-rich-rule='
rule family="ipv4"
source address="172.20.2.10"
port port="8080" protocol="tcp"
accept' --permanent
firewall-cmd --zone=dmz --add-rich-rule='
rule family="ipv4"
source address="172.20.2.10"
protocol value="icmp"
accept' --permanent
firewall-cmd --zone=dmz --add-rich-rule='
rule family="ipv4"
source address="172.20.3.30"
service name="ssh"
accept' --permanent
firewall-cmd --zone=dmz --set-target=DROP --permanent
firewall-cmd --set-log-denied=all
firewall-cmd --reload
firewall-cmd --zone=dmz --list-all
[Speaker Notes: firewall-cmd --zone=dmz --remove-service=ssh --permanent 2>/dev/null || true firewall-cmd --zone=dmz --remove-service=http --permanent 2>/dev/null || true firewall-cmd --zone=dmz --add-rich-rule=' rule family="ipv4" source address="172.20.2.10" port port="8080" protocol="tcp" accept' --permanent firewall-cmd --zone=dmz --add-rich-rule=' rule family="ipv4" source address="172.20.2.10" protocol value="icmp" accept' --permanent firewall-cmd --zone=dmz --add-rich-rule=' rule family="ipv4" source address="172.20.3.30" service name="ssh" accept' --permanent firewall-cmd --zone=dmz --set-target=DROP --permanent firewall-cmd --set-log-denied=all firewall-cmd --reload firewall-cmd --zone=dmz --list-all]

---
Part 3 — Node 2 (Web/App Server) Configuration — BASH
cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF'
<?xml version="1.0" encoding="utf-8"?>
<whitelist>
<command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/>
<user id="0"/>
</whitelist>
EOF
grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf
sed -i 's/^Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf
firewall-cmd --reload
[Speaker Notes: cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF' <?xml version="1.0" encoding="utf-8"?> <whitelist> <command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/> <user id="0"/> </whitelist> EOF grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf sed -i 's/^Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf firewall-cmd --reload]

---
Part 4 — Node 3 (Database Server) Configuration
◆ Step 4.1 — Zone assignment
◆ Step 4.2 — Internal zone: PostgreSQL from node2 only; SSH from management only
◆ Step 4.3 — Lockdown on node3
[Speaker Notes: ```bash podman exec -it node3 bash ``` ### Step 4.1 — Zone assignment ```bash firewall-cmd --zone=internal --add-interface=eth0 --permanent firewall-cmd --reload ``` ### Step 4.2 — Internal zone: PostgreSQL from node2 only; SSH from management only ```bash firewall-cmd --zone=internal --remove-service=ssh --permanent 2>/dev/null || true firewall-cmd --zone=internal --remove-service=dhcpv6-client --permanent 2>/dev/null || true firewall-cmd --zone=internal --add-rich-rule=' rule family="ipv4" source address="172.20.2.20" port port="5432" protocol="tcp" accept' --permanent firewall-cmd --zone=internal --add-rich-rule=' rule family="ipv4" source address="172.20.3.30" service name="ssh" accept' --permanent firewall-cmd --zone=internal --add-rich-rule=' rule family="ipv4" source address="172.20.3.30" protocol value="icmp" accept' --permanent firewall-cmd --zone=internal --set-target=DROP --permanent firewall-cmd --set-log-denied=all firewall-cmd --reload firewall-cmd --zone=internal --list-all ``` ### Step 4.3 — Lockdown on node3 ```bash cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF' <?xml version="1.0" encoding="utf-8"?> <whitelist> <command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/> <user id="0"/> </whitelist> EOF grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf sed -i 's/^Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf firewall-cmd --reload ``` ---]

---
Part 4 — Node 3 (Database Server) Configuration — BASH
podman exec -it node3 bash
firewall-cmd --zone=internal --add-interface=eth0 --permanent
firewall-cmd --reload
[Speaker Notes: podman exec -it node3 bash firewall-cmd --zone=internal --add-interface=eth0 --permanent firewall-cmd --reload]

---
Part 4 — Node 3 (Database Server) Configuration — BASH
firewall-cmd --zone=internal --remove-service=ssh --permanent 2>/dev/null || true
firewall-cmd --zone=internal --remove-service=dhcpv6-client --permanent 2>/dev/null || true
firewall-cmd --zone=internal --add-rich-rule='
rule family="ipv4"
source address="172.20.2.20"
port port="5432" protocol="tcp"
accept' --permanent
firewall-cmd --zone=internal --add-rich-rule='
rule family="ipv4"
source address="172.20.3.30"
service name="ssh"
accept' --permanent
firewall-cmd --zone=internal --add-rich-rule='
rule family="ipv4"
source address="172.20.3.30"
protocol value="icmp"
accept' --permanent
firewall-cmd --zone=internal --set-target=DROP --permanent
firewall-cmd --set-log-denied=all
firewall-cmd --reload
firewall-cmd --zone=internal --list-all
[Speaker Notes: firewall-cmd --zone=internal --remove-service=ssh --permanent 2>/dev/null || true firewall-cmd --zone=internal --remove-service=dhcpv6-client --permanent 2>/dev/null || true firewall-cmd --zone=internal --add-rich-rule=' rule family="ipv4" source address="172.20.2.20" port port="5432" protocol="tcp" accept' --permanent firewall-cmd --zone=internal --add-rich-rule=' rule family="ipv4" source address="172.20.3.30" service name="ssh" accept' --permanent firewall-cmd --zone=internal --add-rich-rule=' rule family="ipv4" source address="172.20.3.30" protocol value="icmp" accept' --permanent firewall-cmd --zone=internal --set-target=DROP --permanent firewall-cmd --set-log-denied=all firewall-cmd --reload firewall-cmd --zone=internal --list-all]

---
Part 4 — Node 3 (Database Server) Configuration — BASH
cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF'
<?xml version="1.0" encoding="utf-8"?>
<whitelist>
<command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/>
<user id="0"/>
</whitelist>
EOF
grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf
sed -i 's/^Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf
firewall-cmd --reload
[Speaker Notes: cat > /etc/firewalld/lockdown-whitelist.xml << 'EOF' <?xml version="1.0" encoding="utf-8"?> <whitelist> <command name="/usr/bin/python3 -s /usr/bin/firewall-cmd*"/> <user id="0"/> </whitelist> EOF grep -q "^Lockdown=" /etc/firewalld/firewalld.conf || echo "Lockdown=yes" >> /etc/firewalld/firewalld.conf sed -i 's/^Lockdown=.*/Lockdown=yes/' /etc/firewalld/firewalld.conf firewall-cmd --reload]

---
Part 5 — Auditd Configuration (All Nodes)
Run these commands on each node:
[Speaker Notes: Run these commands on each node: ```bash dnf install -y audit 2>/dev/null || true systemctl enable --now auditd auditctl -w /etc/firewalld/ -p wa -k firewall-config-change cat >> /etc/audit/rules.d/firewalld.rules << 'EOF' -w /etc/firewalld/ -p wa -k firewall-config-change -w /usr/lib/firewalld/ -p wa -k firewall-pkg-change EOF ``` ---]

---
Part 5 — Auditd Configuration (All Nodes) — BASH
dnf install -y audit 2>/dev/null || true
systemctl enable --now auditd
auditctl -w /etc/firewalld/ -p wa -k firewall-config-change
cat >> /etc/audit/rules.d/firewalld.rules << 'EOF'
-w /etc/firewalld/ -p wa -k firewall-config-change
-w /usr/lib/firewalld/ -p wa -k firewall-pkg-change
EOF
[Speaker Notes: dnf install -y audit 2>/dev/null || true systemctl enable --now auditd auditctl -w /etc/firewalld/ -p wa -k firewall-config-change cat >> /etc/audit/rules.d/firewalld.rules << 'EOF' -w /etc/firewalld/ -p wa -k firewall-config-change -w /usr/lib/firewalld/ -p wa -k firewall-pkg-change EOF]

---
Part 6 — Verification Tests
Run all verification tests from the host machine unless noted.
◆ Test 6.1 — External zone enforcement (node1)
Expected: services = http https, target = DROP, masquerade = yes
◆ Test 6.2 — Port forward is present
Expected: two entries forwarding 443→8080 and 80→8080 to 172.20.2.20
◆ Test 6.3 — Connectivity node1 → node2 (HTTP)
◆ Test 6.4 — node2 cannot reach node3 on disallowed ports
◆ Test 6.5 — LogDenied produces journal entries
[Speaker Notes: ◆ Test 6.6 — Lockdown is active Expected: all return yes ◆ Test 6.7 — nftables rate-limit table on node1 Expected: table with burstblocked set and inputhttp_guard chain at priority -2 ◆ Test 6.8 — nftables ruleset shows both tables on node1 Expected output includes: ◆ Test 6.9 — Audit rules are in place ◆ Test 6.10 — Policy forwarding works Expected: policies ext-to-dmz, dmz-to-ext, int-to-ext Run all verification tests from the **host machine** unless noted. ### Test 6.1 — External zone enforcement (node1) ```bash podman exec node1 bash -c " echo '=== External zone services ===' firewall-cmd --zone=external --list-all echo '=== Target ===' firewall-cmd --zone=external --get-target echo '=== Masquerade ===' firewall-cmd --zone=external --query-masquerade " ``` Expected: services = http https, target = DROP, masquerade = yes ### Test 6.2 — Port forward is present ```bash podman exec node1 bash -c " firewall-cmd --zone=external --list-forward-ports " ``` Expected: two entries forwarding 443→8080 and 80→8080 to 172.20.2.20 ### Test 6.3 — Connectivity node1 → node2 (HTTP) ```bash podman exec node1 bash -c " curl --connect-timeout 3 http://172.20.2.20:8080 2>&1 | head -5 || echo 'Connection attempt made' " ``` ### Test 6.4 — node2 cannot reach node3 on disallowed ports ```bash podman exec node2 bash -c " # This should be blocked (only 5432 is allowed, and only from node2's IP) # Try port 22 from node2 to node3 curl --connect-timeout 2 http://172.20.3.30:22 2>&1 || echo 'Blocked as expected' " ``` ### Test 6.5 — LogDenied produces journal entries ```bash podman exec node2 bash -c " curl --connect-timeout 2 http://172.20.3.30:9999 2>/dev/null || true " podman exec node3 bash -c " journalctl -k --grep='filter_IN' --since='1 minute ago' " ``` ### Test 6.6 — Lockdown is active ```bash for node in node1 node2 node3; do echo -n "$node lockdown: " podman exec $node firewall-cmd --query-lockdown done ``` Expected: all return `yes` ### Test 6.7 — nftables rate-limit table on node1 ```bash podman exec node1 bash -c " nft list table inet http_guard " ``` Expected: table with `burst_blocked` set and `input_http_guard` chain at priority -2 ### Test 6.8 — nftables ruleset shows both tables on node1 ```bash podman exec node1 bash -c " nft list ruleset | grep '^table' " ``` Expected output includes: ``` table inet firewalld { ... table inet http_guard { ... ``` ### Test 6.9 — Audit rules are in place ```bash for node in node1 node2 node3; do echo "=== $node ===" podman exec $node bash -c "auditctl -l 2>/dev/null | grep firewall || echo 'auditd not running'" done ``` ### Test 6.10 — Policy forwarding works ```bash podman exec node1 bash -c " firewall-cmd --list-all-policies " ``` Expected: policies `ext-to-dmz`, `dmz-to-ext`, `int-to-ext` ---]

---
Part 6 — Verification Tests — BASH
podman exec node1 bash -c "
echo '=== External zone services ==='
firewall-cmd --zone=external --list-all
echo '=== Target ==='
firewall-cmd --zone=external --get-target
echo '=== Masquerade ==='
firewall-cmd --zone=external --query-masquerade
"
podman exec node1 bash -c "
firewall-cmd --zone=external --list-forward-ports
"
podman exec node1 bash -c "
curl --connect-timeout 3 http://172.20.2.20:8080 2>&1 | head -5 || echo 'Connection attempt made'
"
podman exec node2 bash -c "
# This should be blocked (only 5432 is allowed, and only from node2's IP)
# Try port 22 from node2 to node3
curl --connect-timeout 2 http://172.20.3.30:22 2>&1 || echo 'Blocked as expected'
"
podman exec node2 bash -c "
curl --connect-timeout 2 http://172.20.3.30:9999 2>/dev/null || true
"
podman exec node3 bash -c "
[Speaker Notes: podman exec node1 bash -c " echo '=== External zone services ===' firewall-cmd --zone=external --list-all echo '=== Target ===' firewall-cmd --zone=external --get-target echo '=== Masquerade ===' firewall-cmd --zone=external --query-masquerade " podman exec node1 bash -c " firewall-cmd --zone=external --list-forward-ports " podman exec node1 bash -c " curl --connect-timeout 3 http://172.20.2.20:8080 2>&1 | head -5 || echo 'Connection attempt made' " podman exec node2 bash -c " # This should be blocked (only 5432 is allowed, and only from node2's IP) # Try port 22 from node2 to node3 curl --connect-timeout 2 http://172.20.3.30:22 2>&1 || echo 'Blocked as expected' " podman exec node2 bash -c " curl --connect-timeout 2 http://172.20.3.30:9999 2>/dev/null || true " podman exec node3 bash -c " journalctl -k --grep='filter_IN' --since='1 minute ago' "]

---
Part 6 — Verification Tests — BASH (cont. 2)
journalctl -k --grep='filter_IN' --since='1 minute ago'
"
[Speaker Notes: podman exec node1 bash -c " echo '=== External zone services ===' firewall-cmd --zone=external --list-all echo '=== Target ===' firewall-cmd --zone=external --get-target echo '=== Masquerade ===' firewall-cmd --zone=external --query-masquerade " podman exec node1 bash -c " firewall-cmd --zone=external --list-forward-ports " podman exec node1 bash -c " curl --connect-timeout 3 http://172.20.2.20:8080 2>&1 | head -5 || echo 'Connection attempt made' " podman exec node2 bash -c " # This should be blocked (only 5432 is allowed, and only from node2's IP) # Try port 22 from node2 to node3 curl --connect-timeout 2 http://172.20.3.30:22 2>&1 || echo 'Blocked as expected' " podman exec node2 bash -c " curl --connect-timeout 2 http://172.20.3.30:9999 2>/dev/null || true " podman exec node3 bash -c " journalctl -k --grep='filter_IN' --since='1 minute ago' "]

---
Part 6 — Verification Tests — BASH
for node in node1 node2 node3; do
echo -n "$node lockdown: "
podman exec $node firewall-cmd --query-lockdown
done
podman exec node1 bash -c "
nft list table inet http_guard
"
podman exec node1 bash -c "
nft list ruleset | grep '^table'
"
[Speaker Notes: for node in node1 node2 node3; do echo -n "$node lockdown: " podman exec $node firewall-cmd --query-lockdown done podman exec node1 bash -c " nft list table inet http_guard " podman exec node1 bash -c " nft list ruleset | grep '^table' "]

---
Part 6 — Verification Tests — Code
table inet firewalld { ...
table inet http_guard { ...
[Speaker Notes: table inet firewalld { ... table inet http_guard { ...]

---
Part 6 — Verification Tests — BASH
for node in node1 node2 node3; do
echo "=== $node ==="
podman exec $node bash -c "auditctl -l 2>/dev/null | grep firewall || echo 'auditd not running'"
done
podman exec node1 bash -c "
firewall-cmd --list-all-policies
"
[Speaker Notes: for node in node1 node2 node3; do echo "=== $node ===" podman exec $node bash -c "auditctl -l 2>/dev/null | grep firewall || echo 'auditd not running'" done podman exec node1 bash -c " firewall-cmd --list-all-policies "]

---
Part 7 — Hardening Review Checklist
Use this checklist as a self-assessment. Every item should be ✅.
◆ node1 (Gateway)
• [ ] external zone target = DROP
• [ ] external zone services = http, https only
• [ ] Masquerade enabled on external zone
• [ ] Port forwards for 80→8080 and 443→8080 to node2
• [ ] Policies: ext-to-dmz, dmz-to-ext, int-to-ext
• [ ] ICMP blocks on external (echo-request, echo-reply)
[Speaker Notes: • [ ] Rate limiting table http_guard present in nftables • [ ] LogDenied = all • [ ] Lockdown = yes • [ ] Auditd watching /etc/firewalld/ • [ ] No SSH in external zone ◆ node2 (Web/App) • [ ] dmz zone target = DROP • [ ] Port 8080 allowed only from node1's DMZ IP (172.20.2.10) • [ ] ICMP allowed only from node1's DMZ IP (172.20.2.10) • [ ] SSH allowed only from management host (172.20.3.30) ◆ node3 (Database) • [ ] internal zone target = DROP • [ ] Port 5432 allowed only from node2's IP (172.20.2.20) • [ ] ICMP allowed only from management host (172.20.3.30) • [ ] No other ports open Use this checklist as a self-assessment. Every item should be ✅. ### node1 (Gateway) - [ ] `external` zone target = DROP - [ ] `external` zone services = http, https only - [ ] Masquerade enabled on `external` zone - [ ] Port forwards for 80→8080 and 443→8080 to node2 - [ ] Policies: ext-to-dmz, dmz-to-ext, int-to-ext - [ ] ICMP blocks on external (echo-request, echo-reply) - [ ] Rate limiting table `http_guard` present in nftables - [ ] LogDenied = all - [ ] Lockdown = yes - [ ] Auditd watching `/etc/firewalld/` - [ ] No SSH in external zone ### node2 (Web/App) - [ ] `dmz` zone target = DROP - [ ] Port 8080 allowed only from node1's DMZ IP (172.20.2.10) - [ ] ICMP allowed only from node1's DMZ IP (172.20.2.10) - [ ] SSH allowed only from management host (172.20.3.30) - [ ] LogDenied = all - [ ] Lockdown = yes - [ ] Auditd watching `/etc/firewalld/` ### node3 (Database) - [ ] `internal` zone target = DROP - [ ] Port 5432 allowed only from node2's IP (172.20.2.20) - [ ] SSH allowed only from management host (172.20.3.30) - [ ] ICMP allowed only from management host (172.20.3.30) - [ ] No other ports open - [ ] LogDenied = all - [ ] Lockdown = yes - [ ] Auditd watching `/etc/firewalld/` ---]

---
Part 8 — nftables Deep-Dive Verification
Perform these checks to verify the nftables layer matches the firewalld configuration.
◆ 8.1 — Verify DROP target on all three nodes
◆ 8.2 — Verify rich rule presence in nftables on node2
Expected: rules matching ip saddr 172.20.2.10 for TCP 8080 and ICMP
◆ 8.3 — Verify NAT chain on node1
Expected: masquerade statement in the chain
◆ 8.4 — Verify DNAT for port forward on node1
Expected: DNAT rules redirecting 443 and 80 to 172.20.2.20:8080
[Speaker Notes: Perform these checks to verify the nftables layer matches the firewalld configuration. ### 8.1 — Verify DROP target on all three nodes ```bash for node in node1 node2 node3; do echo "=== $node ===" podman exec $node bash -c " for zone in \$(firewall-cmd --get-active-zones | grep -v interfaces); do target=\$(firewall-cmd --zone=\$zone --get-target 2>/dev/null) echo \"Zone: \$zone Target: \$target\" done " done ``` ### 8.2 — Verify rich rule presence in nftables on node2 ```bash podman exec node2 bash -c " nft list chain inet firewalld filter_IN_dmz_allow " ``` Expected: rules matching `ip saddr 172.20.2.10` for TCP 8080 and ICMP ### 8.3 — Verify NAT chain on node1 ```bash podman exec node1 bash -c " nft list chain inet firewalld nat_POST_external " ``` Expected: `masquerade` statement in the chain ### 8.4 — Verify DNAT for port forward on node1 ```bash podman exec node1 bash -c " nft list chain inet firewalld nat_PRE_external " ``` Expected: DNAT rules redirecting 443 and 80 to 172.20.2.20:8080 ---]

---
Part 8 — nftables Deep-Dive Verification — BASH
for node in node1 node2 node3; do
echo "=== $node ==="
podman exec $node bash -c "
for zone in \$(firewall-cmd --get-active-zones | grep -v interfaces); do
target=\$(firewall-cmd --zone=\$zone --get-target 2>/dev/null)
echo \"Zone: \$zone Target: \$target\"
done
"
done
podman exec node2 bash -c "
nft list chain inet firewalld filter_IN_dmz_allow
"
podman exec node1 bash -c "
nft list chain inet firewalld nat_POST_external
"
podman exec node1 bash -c "
nft list chain inet firewalld nat_PRE_external
"
[Speaker Notes: for node in node1 node2 node3; do echo "=== $node ===" podman exec $node bash -c " for zone in \$(firewall-cmd --get-active-zones | grep -v interfaces); do target=\$(firewall-cmd --zone=\$zone --get-target 2>/dev/null) echo \"Zone: \$zone Target: \$target\" done " done podman exec node2 bash -c " nft list chain inet firewalld filter_IN_dmz_allow " podman exec node1 bash -c " nft list chain inet firewalld nat_POST_external " podman exec node1 bash -c " nft list chain inet firewalld nat_PRE_external "]

---
Part 9 — Bonus Challenges
These are optional extensions for students who want to go further.
◆ Bonus 1 — IPv6 support
Extend the configuration to handle IPv6 traffic:
• Assign IPv6 addresses to container interfaces
• Configure firewalld zones to accept/reject IPv6 traffic appropriately
• Update rich rules and rate-limiting to cover ip6 saddr
◆ Bonus 2 — IPSet-based blocklist
◆ Bonus 3 — nftables flowtable for node1 forwarding
[Speaker Notes: ◆ Bonus 4 — Automated compliance check script Write a shell script that: → Iterates over all three nodes → Checks each item in the Part 7 checklist → Outputs PASS/FAIL per item → Returns exit code 0 if all pass, 1 if any fail These are optional extensions for students who want to go further. ### Bonus 1 — IPv6 support Extend the configuration to handle IPv6 traffic: - Assign IPv6 addresses to container interfaces - Configure firewalld zones to accept/reject IPv6 traffic appropriately - Update rich rules and rate-limiting to cover `ip6 saddr` ### Bonus 2 — IPSet-based blocklist ```bash firewall-cmd --new-ipset=country-block --type=hash:net --permanent firewall-cmd --ipset=country-block --add-entry=192.0.2.0/24 --permanent firewall-cmd --ipset=country-block --add-entry=198.51.100.0/24 --permanent firewall-cmd --zone=external --add-rich-rule=' rule source ipset="country-block" drop' --permanent firewall-cmd --reload ``` ### Bonus 3 — nftables flowtable for node1 forwarding ```bash cat > /etc/nftables.d/flowtable.nft << 'EOF' table inet fastpath { flowtable ft { hook ingress priority filter; devices = { eth0, eth1, eth2 }; } chain forward { type filter hook forward priority filter; ip protocol { tcp, udp } flow offload @ft } } EOF nft -f /etc/nftables.d/flowtable.nft nft list flowtable inet fastpath ft ``` ### Bonus 4 — Automated compliance check script Write a shell script that: 1. Iterates over all three nodes 2. Checks each item in the Part 7 checklist 3. Outputs PASS/FAIL per item 4. Returns exit code 0 if all pass, 1 if any fail ---]

---
Part 9 — Bonus Challenges — BASH
firewall-cmd --new-ipset=country-block --type=hash:net --permanent
firewall-cmd --ipset=country-block --add-entry=192.0.2.0/24 --permanent
firewall-cmd --ipset=country-block --add-entry=198.51.100.0/24 --permanent
firewall-cmd --zone=external --add-rich-rule='
rule source ipset="country-block" drop' --permanent
firewall-cmd --reload
cat > /etc/nftables.d/flowtable.nft << 'EOF'
table inet fastpath {
flowtable ft {
hook ingress priority filter;
devices = { eth0, eth1, eth2 };
}
chain forward {
type filter hook forward priority filter;
ip protocol { tcp, udp } flow offload @ft
}
}
EOF
nft -f /etc/nftables.d/flowtable.nft
nft list flowtable inet fastpath ft
[Speaker Notes: firewall-cmd --new-ipset=country-block --type=hash:net --permanent firewall-cmd --ipset=country-block --add-entry=192.0.2.0/24 --permanent firewall-cmd --ipset=country-block --add-entry=198.51.100.0/24 --permanent firewall-cmd --zone=external --add-rich-rule=' rule source ipset="country-block" drop' --permanent firewall-cmd --reload cat > /etc/nftables.d/flowtable.nft << 'EOF' table inet fastpath { flowtable ft { hook ingress priority filter; devices = { eth0, eth1, eth2 }; } chain forward { type filter hook forward priority filter; ip protocol { tcp, udp } flow offload @ft } } EOF nft -f /etc/nftables.d/flowtable.nft nft list flowtable inet fastpath ft]

---
Part 10 — Capstone Teardown
[Speaker Notes: ```bash ~/firewalld-lab/reset-lab.sh for node in node1 node2 node3; do echo "=== $node after reset ===" podman exec $node firewall-cmd --get-default-zone podman exec $node firewall-cmd --zone=public --list-all done ``` ---]

---
Part 10 — Capstone Teardown — BASH
~/firewalld-lab/reset-lab.sh
for node in node1 node2 node3; do
echo "=== $node after reset ==="
podman exec $node firewall-cmd --get-default-zone
podman exec $node firewall-cmd --zone=public --list-all
done
[Speaker Notes: ~/firewalld-lab/reset-lab.sh for node in node1 node2 node3; do echo "=== $node after reset ===" podman exec $node firewall-cmd --get-default-zone podman exec $node firewall-cmd --zone=public --list-all done]

---
Capstone Completion Criteria
You have successfully completed the capstone if:
→ All items in the Part 7 checklist are ✅
→ All Part 6 verification tests pass
→ Part 8 nftables verification commands show expected output
→ You can explain why each rule exists and which module taught it
→ You can recover any node from a simulated locked-out state using podman exec
[Speaker Notes: You have successfully completed the capstone if: 1. All items in the Part 7 checklist are ✅ 2. All Part 6 verification tests pass 3. Part 8 nftables verification commands show expected output 4. You can explain **why** each rule exists and **which module** taught it 5. You can recover any node from a simulated locked-out state using `podman exec` ---]

---
Skills Demonstrated
By completing this capstone, you have demonstrated:
Congratulations on completing the firewalld course! See cheatsheet.md for a quick-reference summary and faq.md for answers to common questions.
[Speaker Notes: By completing this capstone, you have demonstrated: | Skill | Evidence | |-------|---------| | Zone design | Three-zone topology with correct interface assignments | | Service/port control | Precise allow-lists per tier with DROP defaults | | Rich rules | Source-restricted access to 8080, 5432, SSH | | NAT/masquerade | Internet forwarding for DMZ and Internal | | Port forwarding | DNAT from external 443/80 to internal 8080 | | Inter-zone policies | Three policies governing forwarding paths | | Logging | LogDenied=all on all nodes; journal verification | | Rate limiting | Custom nftables meter with dynamic auto-block set | | Lockdown | D-Bus protection on all three nodes | | Auditd integration | Config-change audit rules on all nodes | | nftables fluency | Direct nft verification of every firewalld decision | | Troubleshooting | Five-question methodology applied in verification tests | --- *Congratulations on completing the firewalld course!* *See [cheatsheet.md](cheatsheet.md) for a quick-reference summary and [faq.md](faq.md) for answers to common questions.*]

---
Skills Demonstrated
Skill	Evidence
Zone design	Three-zone topology with correct interface assignments
Service/port control	Precise allow-lists per tier with DROP defaults
Rich rules	Source-restricted access to 8080, 5432, SSH
NAT/masquerade	Internet forwarding for DMZ and Internal
Port forwarding	DNAT from external 443/80 to internal 8080
Inter-zone policies	Three policies governing forwarding paths
Logging	LogDenied=all on all nodes; journal verification
Rate limiting	Custom nftables meter with dynamic auto-block set
Lockdown	D-Bus protection on all three nodes
Auditd integration	Config-change audit rules on all nodes
nftables fluency	Direct nft verification of every firewalld decision
Troubleshooting	Five-question methodology applied in verification tests
[Speaker Notes: Skill | Evidence ------------------------------------------------------------ Zone design | Three-zone topology with correct interface assignments Service/port control | Precise allow-lists per tier with DROP defaults Rich rules | Source-restricted access to 8080, 5432, SSH NAT/masquerade | Internet forwarding for DMZ and Internal Port forwarding | DNAT from external 443/80 to internal 8080 Inter-zone policies | Three policies governing forwarding paths Logging | LogDenied=all on all nodes; journal verification Rate limiting | Custom nftables meter with dynamic auto-block set Lockdown | D-Bus protection on all three nodes Auditd integration | Config-change audit rules on all nodes nftables fluency | Direct nft verification of every firewalld decision Troubleshooting | Five-question methodology applied in verification tests]